## Slide 1: A computational simulation of neuromuscular block monitor sensitivity to procedural variability
Ryan Spears, Taylor Tew, Katie Carroll
12/12/17

## Slide 2: Agenda
Background
Methods
Results
Conclusions

## Slide 3: Agenda
Background
Methods
Results
Conclusions

## Slide 4: Neuromuscular Block Monitoring
Neuromuscular blocking agents (NMBAs)
Electromyography-based monitoring systems
NeuroMuscular Transmission (NMT)
Train-of-four (TOF) stimulation pattern: four 300𝜇s pulses at 2Hz

## Slide 5: Clinical Observation
Increased subcutaneous fat thickness requires higher stimulation currents
  Fat increases electrode-to-fiber distance
  Fat insulates the fiber
  Fat makes accurate electrode placement harder
Notes: Investigative strategy:
  Electrode-to-fiber distance
  Fat thickness
  Lateral electrode placement

## Slide 6: Agenda
Background
Methods
Results
Conclusions

## Slide 7: COMSOL Model
Skin-Fat-Muscle Interface
Geometry & Material Properties
  Quasistatic Approximation
Boundary Conditions
  Large Volume
Variability:
  Fat Thickness (0.1in - 1in)
  Electrode to Fiber Lateral Distance (0-1 in)
  Current Stimulus (0 - 20 mA)
Nerve fiber positioned in 3D tissue COMSOL model with parameter variation
Notes: Investigative strategy:
  Electrode-to-fiber distance
  Fat thickness
  Lateral electrode placement

## Slide 8: Lateral Electrode Position/Fat Thickness
Nerve Position held at constant Z-coordinate
Variation in Fat Thickness
Variation in Electrode-to-fiber lateral distance
Notes: Investigative strategy:
  Electrode-to-fiber distance
  Fat thickness
  Lateral electrode placement

## Slide 9: COMSOL Validation
Analytic Point Source vs. Experimental COMSOL Point Source Voltage in Homogeneous medium
Point (x,y,z) | COMSOL (V) | Analytical (V) | % Diff
-3, 1, 1 | 1.668 | 1.700 | 1.88%
-1, 0.5, -0.5 | 0.6928 | 0.6997 | 0.98%
0,0,0 | 5.022E-5 | 0 | 0%
-0.5, -0.5, -0.75 | 0.3054 | 0.2928 | 4.30%
4, 0, 0 | -2.6300 | -2.6854 | 2.06%
Point Source Voltage Distribution in COMSOL
Notes: Investigative strategy:
  Electrode-to-fiber distance
  Fat thickness
  Lateral electrode placement

## Slide 10: NEURON & MATLAB
Interpolate voltages to internodal length
Simple single axon model:
  Diameter: 20𝜇m
  Length: 20.1cm (12.7cm from distal electrode)
Input voltages as nodal extracellular voltage sources
Action potential generation at terminal node interpreted as muscle activation

## Slide 11: Agenda
Background
Methods
Results
Conclusions

## Slide 12: Current Stimulus
Lateral electrode distance and fat thickness held constant at 0.3 inches
Increasing current produced larger second differences
Second differences of extracellular voltage along the length of the axon for three current amplitudes.

## Slide 13: Fat Thickness
Lateral electrode distance held constant at 0.3 inches with a 5 mA current stimulus
Increasing fat produced smaller second differences
Second differences of extracellular voltage along the length of the axon for three lateral electrode positions.

## Slide 14: Lateral Electrode Distance
Fat thickness held constant at 0.3 inches with a 3.75 mA current stimulus
Increasing lateral distance from the electrode produced smaller second differences
Second differences of extracellular voltage along the length of the axon for three lateral electrode positions

## Slide 15: Summary
Increasing fat thickness and lateral electrode position have compounding effects on threshold current
Binary chart of action potential generation with parameter variation.
0: no action potential
1: action potential

## Slide 16
The contribution of fat thickness to second differences (bottom) was isolated by taking the difference of the second differences generated with constant fat thickness (top) and varied fat thickness (middle).
(middle)
Δdepth = fat
(top)
Δdepth = muscle
Isolating Fat Content Contributation

## Slide 17
Isolating Fat Content Contributation

## Slide 18
Numerator
Denominator

## Slide 19
Electrode-to-fiber distance impacts second difference voltages more so than fat content
The relative contribution of electrode-to-fiber depth and fat thickness to second differences of extracellular voltage.
>1: predominance of electrode-to-fiber distance
<1: predominance of fat thickness
Isolating Fat Content Contributation

## Slide 20: Agenda
Background
Methods
Results
Conclusions

## Slide 21: Conclusions
Strength-Distance relationship predominates clinical observation
  Electrode-to-Fiber Distance > Isolated Fat Content
  Lateral Electrode Placement > Isolated Fat Content
Model/Study improvements:
  COMSOL: nerve anatomy
  NEURON: motor units/pools & graded output
  Parallel clinical study

## Slide 22: Questions?

## Slide 23: Supplementary Material

## Slide 24: Supplementary Material: COMSOL
Volume Change Validation
Material Properties Table
 | X- Coordinate | Y- Coordinate | Z- Coordinate
Change in Voltage | -0.0082 | -0.0032 | -0.0117
% Diff | 0.4686% | 0.1825% | 0.6727%